## Slide 1: EE 445L – Embedded System Design Lab
Brushed DC Motors
(not covered AC motors: induction, synchronous)
For more information read Section 6.5 in the book
http://www.teslamotors.com/blog/induction-versus-dc-brushless-motors

## Slide 2: Motor EM
2

## Slide 3: DC Motor Physics
3
http://www.electricaleasy.com/2014/01/basic-working-of-dc-motor.html
Force = Current*Length*Magnetic Field

## Slide 4: PWM DC Motor Interface
For more information read Section 6.5.4 in the book
R=30Ω
Why is I > (V-VCE)/30Ω?
IRLD024

## Slide 5: Darlington Transistor
TIP120 (NPN)
hfe = 1000
Ice = 3A
Ib = Icoil /hfe = 1A/1000 = 1mA
Rb ≤ (VOH-Vbe)/Ib = (3-2.5)/1mA = 0.5 kW
Rb = 100 W
VCE depends on current
+5V
TM4C123 not LM4F120

## Slide 6: Power MOSFET (IRLD024 or IRLD120 )
VGS = 3.3V turns it on
IDS = 2.5A max, need 0.1A
Rb = 10kW (just to limit transients)
VDS depends on current
Current depends on VDS
+5V
IRLD024
G
D
S
M2
M1

## Slide 7: IRLD024 or IRLD120
Got VGS = 3.3V
Need IDS = 0.1A

## Slide 8: IRLD024 or IRLD120
Got VGS = 3.3V
Need IDS = 0.1A

## Slide 9: DC Motor PWM Software
void PWM0A_Init(uint16_t period,
uint16_t duty){
SYSCTL_RCGCPWM_R |= 0x01; // 1) activate PWM0
SYSCTL_RCGCGPIO_R |= 0x02; // 2) activate port B
while((SYSCTL_PRGPIO_R&0x02) == 0){};
GPIO_PORTB_AFSEL_R |= 0x40; // alt funct on PB6
GPIO_PORTB_PCTL_R =
(GPIO_PORTB_PCTL_R&0xF0FFFFFF)+0x04000000; // PWM0
GPIO_PORTB_AMSEL_R &= ~0x40; // disable analog on PB6
GPIO_PORTB_DEN_R |= 0x40; // enable digital I/O on PB6
SYSCTL_RCC_R = 0x00100000 | // 3) use PWM divider
(SYSCTL_RCC_R & (~0x000E0000)); // 1/2 divider
PWM0_0_CTL_R = 0; // 4) re-loading down-counting mode
PWM0_0_GENA_R = 0xC8; // low on LOAD, high on CMPA down
PWM0_0_LOAD_R = period - 1; // 5) cycles count down to 0
PWM0_0_CMPA_R = duty - 1; // 6) count value output rises
PWM0_0_CTL_R |= 0x00000001; // 7) start PWM0
PWM0_ENABLE_R |= 0x00000001; // enable PB6/M0PWM0
}
Program 6.8 in the book
TM4C123 not LM4F120

## Slide 10: DC Motor PWM
void PWM0A_Duty(uint16_t duty){
PWM_0_CMPA_R = duty - 1; // 6) count value output rises
}
P
B
6
TM4C123
D
r
i
v
e
r
M
o
t
o
r
P
e
r
i
o
d
L
o
w
H
i
g
h
PWM0A_Init(40000, 30000);
// 1000 Hz, 75% duty
Program 6.8 in the book
Period(1ms) = 40000
High is 300 to 39900
Power = Voltage*Current*DutyCycle

## Slide 11: Lab 10 Motor Characterization*
Power = Voltage * Current
1) Measure Power using Lab Bench supply and AMP Meter.
2) Use Scope to measure TACH_OUT Frequency Speed (RPS) = Frequency/4
3) Plot Speed vs. Power (mw)
+
-
motor
TACH_OUT
1N914
BLUE WIRE
RED WIRE
GREEN WIRE
LAB
BENCH
SUPPLY
(VARIABLE)
+5V (max)
YELLOW WIRE
METER
TO SCOPE

## Slide 12: Lab 10 Motor Characterization
+
-
motor
TACH_OUT
1N914
BLUE WIRE
RED WIRE
GREEN WIRE
LAB
BENCH
SUPPLY
(VARIABLE)
+5V (max)
YELLOW WIRE
Tach
I/F
Circuit
TO SCOPE
3.3V
1) Build TACH interface circuit (Lect. 35)
2) Use Scope to confirm hysteresis calculations and correct circuit operation from 80Hz to 200Hz

## Slide 13: Lab 10 Motor Characterization
+
-
motor
TACH_OUT
1N914
BLUE WIRE
RED WIRE
GREEN WIRE
LAB
BENCH
SUPPLY
(VARIABLE)
+5V (max)
YELLOW WIRE
Tach
I/F
Circuit
TM4C
PB4
TO SCOPE
3.3V
3.3V
ST7735
1) Setup period measure SW
2) Confirm RPS using scope and values outputted to LCD
3) Confirm Period calculation
uint32_t Period; // 24-bit, 12.5 ns units
uint32_t static First; // Timer0A first edge, 12.5 ns
int32_t Done; // mailbox status set each rising edge
void Timer0A_Handler(void){
TIMER0_ICR_R = 0x00000004; // acknowledge timer0A
Period = (First - TIMER0_TAR_R) // NOTE: underflow tolerant calculation
& 0x00FFFFFF;
First = TIMER0_TAR_R; // setup for next measurement
Done = 1; // set semaphore
}

## Slide 14: Summary
Brushed DC motor
  Simple,
  Use transistor and PWM
  Requires feedback